A preliminary Seismic Hazard Study in Northern Arizona: Another Look at the b-Value

D.S. Brumbaugh1; D.A. Evanzia1

1.Arizona Earthquake Information Center, Northern Arizona University, Flagstaff, AZ, United States.

The increase in population in northern Arizona and the seismic history of the area that includes the occurrence of damaging events calls for a renewed effort to develop the tools that can be applied to the estimation of seismic hazard. The b-value of the Gutenberg-Richter (GR) law has played a central role in many earthquake hazard related models. The last attempt to develop frequency/magnitude estimates for northern Arizona using the Gutenberg-Richter law was by Giardina in 1977. Since that time coverage of seismic activity and thus the size of the database has greatly improved. As a result, a catalog of northern Arizona seismicity now exists for the time frame 1985-2005 that is considered complete for M≥2.5 This study compares the b-value of the new data set to Giardina's results.

Giardina produced GR regression curves for a region centered on Flagstaff with a radius of 200 miles and for a region centered on Flagstaff with a radius of 60 miles. The 1985-2005 comparison database from this study comes from a region between 34.5N-37N x 110W-113W that includes Flagstaff. Giardina's 200 mile radius area had a b-value of .977 while the 60 mile radius area had a b-value of 1.10. The 1985-2005 data set of this study resulted in a b-value of .917. A second data set of the study area was constructed for 1906-2000 with a minimum catalog completeness of M≥3.5. This resulted in a similar b-value of .903. The b-value results for this study and for Giardina that are less than b=1.0 suggest a somewhat higher stress level for northern Arizona.

Giardina's 60 mile area with b-value of 1.10 indicates a larger number of smaller events than predicted by the GR law and a lower stress level. Further research efforts will focus on reducing the 1985-2005 data set to an area comparable to that of the 60 mile radius area of Giardina to see how the resulting b-values from the new data compares to Giardina's b-value.